## Slide 1: Part A
Front of the truck

## Slide 2: Leveled vehicle, lights, leaks

## Slide 3: Open hood, start with the axle. Wheel first

## Slide 4: Inspect tread depth, Inflation and inside.

## Slide 5: Brakes are next. Rotor, caliper, pads, chamber and hoses.

## Slide 6: Suspension. Mount, leafspring, bushing, u-bolt, shock, upper and lower mounts.

## Slide 7: 3-pc Steering linkage and steering box w/ hose

## Slide 8: Air compressor and power steering pump. Gear driven

## Slide 9: Power steer reservoir and oil level. All other hoses/connections. Check for leaks

## Slide 10: Alternator, belt driven

## Slide 11: Coolant reservoir and related hoses.

## Slide 12: Water pump, belt driven