## Slide 1: Part C

## Slide 2: Head board of the trailer, lights (Clearance)

## Slide 3: Side of the trailer. Body and lights markers at the bottom. Clearance at the top.

## Slide 4: Landing gear and frame crossmembers

## Slide 5: Trailer body cross members.

## Slide 6: Middle marker light (amber): turn signal and hazard.

## Slide 7: Frame and slider box.

## Slide 8: Axle section. Start with the wheel. Tire, rim, lug nuts and hub seal.

## Slide 9: Check tire depth, check for debris in between.

## Slide 10: Brakes: Drum, shoes, slack adjuster / pushrod…

## Slide 11: …brake chamber and brake hoses.

## Slide 12: Suspension: Torque arm, Torque arm mount, bushing, shock, air bag and mounts. NO u-bolts

## Slide 13: Mud flap, no higher than 8” off the ground.

## Slide 14: Door tie, ABS light (amber), rear marker light (and clearance light) red.

## Slide 15: Rear clearance lights, doors, hinges, latches, lift gate.

## Slide 16: Rear lights: Tail lights, brake lights, turn signals and hazards. DOT bumper and reflectors